Parallel Memory
Mageswaran D

---
Terms
- Time l taken by the memory system, to deliver the requested memory word as a block to the processor is called latency.
- The rate at which data can be pumped from the memory to the processor determines the bandwidth of the memory system.
- As an analogy, if water comes out of the end of a fire hose 2 seconds after a hydrant is turned on, then the latency of the system is 2 seconds. Once the flow starts, if the hose pumps water at 1 gallon/second then the 'bandwidth' of the hose is 1 gallon/second. If we need to put out a fire immediately, we might desire a lower latency. This would typically require higher water pressure from the hydrant. On the other hand, if we wish to fight bigger fires, we might desire a higher flow rate, necessitating a wider hose and hydrant.

---
Effect of Memory Latency on Performance
- Processor clock speed = 1GHZ = 1/10^9 = 1ns
- DRAM with latency l = 100ns
- Two MADs which can execute 4 instruction per clock i.e FLOPS/cycle = 4
- Peak processr rating is 4 * 1/1ns = 4GFLOPS
- For a dot operation with a data fetch : single multiply-add / 100ns = 1/100ns = 10MFLOPS

---
 Improving Effective Memory Latency Using Caches
- Cache memory, small on chip memory cloase to processor, acts as a low-latency high-bandwidth storage.
- Cache hit ratio
  - The fraction of data references satisfied by the cache
- Computation Memory bound
  - Computation which depends upon the rate of data that can be pumped into the CPU
- This notion of repeated reference to a data item in a small time window is called temporal locality of reference.

---
Impact of caches on memory system performance
- 1GHZ Processor = 1ns clock
- DRAM 100ns latency
- Cache 32KB with latency 1ns
- Lets see multiply of MatA and MatB (32 x 32)
  - int 32 * 32 = 1024 * 2 bytes = 2048 bytes * 2 = 4K
  - DRAM to Cache : 4K * 100ns = 400us
  - Num of operations : 2n^3 = 2 * 32 ^3 = 64K
  - 4FLOPS/cycle: (64K/4)/1ns = 16us
- Total computation time : 400us + 16us
- Computation rate : 64K/416us = 151MFLOPS

---
Impact of Memory Bandwidth
Memory bandwidth refers to the rate at which data can be moved between the processor and memory.

---
Cont of slide 3...
- Increase the memory block size from one word to 4 words i.e cache lines
- Now Processor can fetch 4 word for every 100 clock cycles
- Considering dot products, for every two access of memory (200cycles), 8 FLOPS (four MADs) can be performed, 25ns/FLOP
- This corresponds to a FLOP every 25 ns, for a peak speed of 40 MFLOPS. This doesn't decrease the latency, however, it increased the bandwidth.

---
Cache In Practical
- 4words = 128 bits is not possible
- Alternative, after first memory fetch (100cycles), consecutive words are send on the memory bus on subsequent bus cycles
- This add extra latency for cache lines to avail for CPU, 100 + 3 * Memory bus cycle
- If memory bus rate is 200MHZ, then 15ns is added extra
- This does not change our bound onthe execution rate significantly.
- Spatial locality of memory access
    - The data layouts were assumed to be such that consecutive data words in memory were used by successive instructions.
- Tiling
    - break the iteration space into blocks and compute the product one block at a time

---
Spatial Locality Explained
- 2D data are stored in column major or row major order.
- Column major:
  - Consecutive column data are stored in consecutive memory location
- Row major:
  - Consecutive row data are stored in consecutive memory location

---
int A[3][4] =  {{19,22,31,42},
                   {50,61,32,83},
                  {93,47,15,66} };
Offset
Row Column Nbytes
A[X][Y]
Row Major
   N ( X * C + Y )
19	22	31	42	50	61	32	83	93	47	15	66
Column Major
N ( X + Y * R )
19	50	93	22	61	47	31	32	15	42	83	66

---
- Stride Access:
  - How far the next memory data in memory block, lies from current memory data, that needs to be pumped to process.
  - How many clock cycles do I need to spend to get next data for processing.
  - If you want next row pixel for processing use row major order, same with column major order
- Large scale vector supercomputers
  - 1 MFLOPS/MBs (the ratio signifies FLOPS per megabyte/second of bandwidth)
- Fast microprocessor based computers
  - 100 MFLOPS/MBs.

---
- Exploiting spatial and temporal locality in applications is critical for amortizing memory latency and increasing effective memory bandwidth.
- Certain applications have inherently greater temporal locality than others, and thus have greater tolerance to low memory bandwidth. The ratio of the number of operations to number of memory accesses is a good indicator of anticipated tolerance to memory bandwidth.
- Memory layouts and organizing computation appropriately can make a significant impact on the spatial and temporal locality.

---
Alternate Approaches for Hiding Memory Latency
- Imagine sitting at your computer browsing the web during peak network traffic hours.
- For better response
  - (i) we anticipate which pages we are going to browse ahead of time and issue requests for them in advance; aka prefetching
  - (ii) we open multiple browsers and access different pages in each browser, thus while we are waiting for one page to load, we could be reading others; aka multithreading, or
  - (iii) we access a whole bunch of pages in one go – amortizing the latency across various accesses. aka spatial locality